## Slide 1: APRS
Bob Houghton - AD6QF - 12/16/20
Automatic Packet Reporting System
Fullerton Radio Club 12/16/20

## Slide 2: APRS
What is it?
a real-time tactical communications and display system (situational awareness)
It was designed to be a resource for the local and traveling ham to show surrounding local information of immediate value.
Is NOT primarily intended as a way to track cars on a map (although it will do that)

## Slide 3: APRS
History
Developed by Bob Bruninga WB4APR (thus the name)
Introduced at the 1992 TAPR/Arrl Digital Communications Conference

## Slide 4: APRS
How it works
Uses packet radio
Original packet radio is point-to-point with ‘connected’ stations
APRS is point-to-many
Packet radio, but unconnected packets (no “ack”)

## Slide 5: APRS
How it works - direct - without the internet
Uses radio, TNC (hardware or software), and (sometimes) a computer
Simplex mode - Generally VHF FM on 144.39 MHz (North America)
Sender’s radio transmits a packet.
Packet can contain callsign, lat/long/altitude/speed/direction, a symbol, status message, telemetry, short messages directed to specific stations
Multiple radios (in simplex range) can receive it.
No ack returned (unless it is a “message”)

## Slide 6: APRS
How it works - using digipeater(s) - without the internet
Sender’s radio transmits a packet.
Packet is received by a digipeater which temporarily stores and then retransmits the packet. Like voice repeaters, digipeaters are generally at a high elevation to cover a large area
Packet can contain callsign, lat/long/altitude/speed/direction, a symbol, status message, telemetry, short messages directed to specific stations
Multiple radios (in simplex range) can receive it.
No ack returned (unless it is a “message”)

## Slide 7: APRS
How it works - using digipeater(s) - combined with the internet
Specialized stations called iGates, pass APRS packets traffic from RF to the internet and vice-versa (requires a radio, TNC, and a computer - often a Raspberry Pi)
A server network (APRS-IS) manages the storing and routing of packets
APRS-IS a common name given to the Internet-based network which inter-connects various APRS radio networks throughout the world (and space)
Other servers can exchange packets with APRS-IS and make them available via the web (aprs.fi, aprsdirect.com, etc.)

## Slide 8: APRS
SSIDs are station designators appended to your callsign
– 0 | Your primary station usually fixed and message capable
-1 | generic additional station, digi, mobile, wx, etc
-2 | generic additional station, digi, mobile, wx, etc
-3 | generic additional station, digi, mobile, wx, etc
-4 | generic additional station, digi, mobile, wx, etc
-5 | Other networks (Dstar, Iphones, Androids, Blackberry's etc
-6 | Special activity, Satellite ops, camping or 6 meters, etc
-7 | walkie talkies, HT's or other human portable
-8 | boats, sailboats, RV's or second main mobile
-9 | Primary Mobile (usually message capable)
-10 | internet, Igates, echolink, winlink, AVRS, APRN, etc
-11 | balloons, aircraft, spacecraft, etc
-12 | APRStt, DTMF, RFID, devices, one-way trackers*, etc
-13 | Weather stations
-14 | Truckers or generally full time drivers
-15 | generic additional station, digi, mobile, wx, etc
a station’s SSID gives you an idea of it’s purpose
The common ones to know are
  -0 for base stations
  -7 for HTs
  -9 for mobile
  Example: AD6QF-7

## Slide 9: APRS
What’s needed?
To observe
  aprs.fi
  aprsdirect.com
To participate
  radio, TNC, computer or tablet
  cellphone or tablet w/app
  APRS capable radio

## Slide 10: APRS
Beaconing vs. messages
Beaconing is a broadcast
  Contains information of interest to the general recipient
  Location, beacon status text, wx information, telemetry

## Slide 11: APRS
Beaconing vs. messages
Messages are station-to-station
But are not private (still packets)
If station A has beaconed recently, it will be known to the APRS-IS network
If station B sends a message to station A, the APRS-IS network will route the message to the last iGate that heard station B

## Slide 12: APRS
APRS-capable radios
Stand-alone (built-in TNC)
  Kenwood TH-d7, d72, d74
  Kenwood TM-700, 710G
  Yaesu FT-8, FT1DR, FT2DR, FT3DR
  Yaesu FTM-100, 300, 350, 400
  Icom has some DPRS radios that send APRS to the internet but do not use analog rf digis
  There are others

## Slide 13: APRS
Other solutions
Mobilnkd 2 ($65) + Computer w/bluetooth or Android device + radio
Moblinkd 3 ($120) + Computer or iOS device (or Android device) + radio
Better than an APRS-capable HT due to detailed map on tablet, computer, or cellphone

## Slide 14: APRS
Non-rf solutions
aprs.fi app for iOS ($7+)
aprsDroid app for android ($5 Google play store or OpenSource supportware)

## Slide 15: APRS
Mobile frequency beaconing
This is a way for hams to “find each other” by announcing the frequency they are currently monitoring.
The frequency of your VFO A is included in the status text of your beacon. Other hams can see this.
When you receive a station with frequency info included in your beacon you press the TUNE button to switch to that frequency

## Slide 16: APRS
Future topics to explore
What are paths?
What does Wide 1-1 mean?
How do I send an APRS message to somebody’s email address?
How do I send and receive aprs messages to SMS?
What is smart beaconing

## Slide 17
Questions?

## Slide 18
Where do we go from here?